AQUAPANEL® Cement Board Floor

Dry floor with reinforced load-distributing layer load

capacity up to 4.0 kN/ m2 (Variant 2)

Specification examples

| Item | Quantity / ME | Description of service | Unit cost | Total cost |
| --- | --- | --- | --- | --- |
|  | m2 m2 m2 m2 m2 m2 m2 | Prepare, clean solid floor for receiving a dry floor. In the case of floors without basements: Apply a moisture barrier in acc. with DIN 18195 made of ___________________________, which is guided approx. _________ cm high (up to further horizontal sealing in the walls). In the case of new concrete floors or above wet rooms: Lay polyethylene film (e.g. 0.2 mm) loosely with 50 cm overlap. AQUAPANEL® levelling fill, installation thickness (d<60mm) ________ mm, must be removed with a superelevation of 10% flat with the plane over gauges. Uneven areas, pipes or cables must be covered by at least 10 mm. Lay Fasoperl® A8 cover panels, 8 mm thick, tight against one another, avoiding cross joints and shifted to the joints on the fill. Lay AQUAPANEL® Cement Board Floor, 22 mm, cement-bonded dry floor element with surrounding groove milling, in accordance with the processing instructions of Knauf Aquapanel GmbH & Co. KG. Lay an additional layer of AQUAPANEL® Cement Board Indoor (12.5 mm cement-bonded building panel) transverse to the laying direction of the AQUAPANEL® Cement Board Floor. Adhesion is carried out by AQUAPANEL® joint adhesive (PU) or AQUAPANEL® groove adhesive (PU) which is applied in beads with a spacing of approx. 10 cm. Apply AQUAPANEL® Cement Board Indoor screwed with AQUAPANEL®- Floor screws 4.2 x 24 mm or AQUAPANEL® Maxi screw 25. |  |  |