AQUAPANEL® Cement Board Floor

Solid floor with dry floor with fill ( 60 mm

Specification examples

| Item | Quantity / ME | Description of service | Unit cost | Total cost |
| --- | --- | --- | --- | --- |
|  | m2 m2 m2 m2 m2 m2 m2 m2 | Prepare, clean solid floor for receiving a dry floor. In the case of floors without basements: Apply a moisture barrier in acc. with DIN 18195 made of ___________________________, which is guided approx. _________ cm high (up to further horizontal sealing in the walls). In the case of new concrete floors or above wet rooms: Lay polyethylene film (e.g. 0.2 mm) loosely with 50 cm overlap. AQUAPANEL® Levelling Fill, installation thickness ________ mm (over 60 mm), must be removed with a superelevation of 10% flat with the plane over gauges. Uneven areas, pipes or cables must be covered by at least 10 mm. Fit mineral fibre impact sound insulation panels 12 – 1 mm, processing in accordance with the details from the manufacturer, tight against one another, avoiding cross joints and shifted to the joints on the fill. Lay AQUAPANEL® Cement Board Floor, 22 mm, cement-bonded dry floor element with surrounding slot, in accordance with the processing instructions of Knauf Aquapanel GmbH & Co. KG. Apply AQUAPANEL® Interior Primer in accordance with the processing instructions of Knauf Aquapanel GmbH & Co. KG. AQUAPANEL® Levelling Fill, maximum or minimum requirement per cm. |  |  |