AQUAPANEL® Cement Board Floor

Sound boarded timber joist floor with dry floor

Specification examples

| Item | Quantity / ME | Description of service | Unit cost | Total cost |
| --- | --- | --- | --- | --- |
|  | m2 m2 m2 m2 m2 m2 m2 m2 m2 | Prepare timber joist floor for receiving a dry floor, remove floor battens, filler and dead floor. Screw new support battens _____/______ cm laterally onto the joists. Distance to upper edge of joists _______ cm. Fit new dead floor made of _________, _______ mm thick. Depending on the requirements as drip protection, fit a layer _____________ (packing paper, glass fibre mat or the like) with 10 cm overlap. Fill AQUAPANEL® Levelling Fill, installation thickness ________ mm, between the joists, remove via their upper edge. Cut cover panels (e.g. soft timber fibres, mineral fibres, plasterboard in accordance with EN520; note material thickness for layer height), in accordance with the clear joist distance and lay between them. Compress the fill on top of laid panels or chip panel strips with a hand stamper. AQUAPANEL® Levelling Fill, installation thickness ________ mm, must be removed with a superelevation of 10% flat with the plane over gauges. Uneven areas, pipes or cables must be covered by at least 10 mm. Uneven areas, pipes or cables must be covered by at least 10 mm. Lay cover panels (e.g. soft timber fibres, mineral fibres, plasterboard in accordance with EN520; note material thickness for layer height), tight against one another, avoiding cross joints and shifted to the joints on the fill. Fills with a height of more than 60 mm are to be mechanically compressed on top of laid panels or chip panel strips with a hand stamper or a light surface vibrator. Lay AQUAPANEL® Cement Board Floor, 22 mm, cement-bonded dry floor element with surrounding slot, in accordance with the processing instructions of Knauf Aquapanel GmbH & Co. KG. AQUAPANEL® Levelling Fill, maximum or minimum requirement per cm. |  |  |