AQUAPANEL® Cement Board Floor

Timber joist floor with dry floor with fill ≤ 200 mm

Specification examples

| Item | Quantity / ME | Description of service | Unit cost | Total cost |
| --- | --- | --- | --- | --- |
|  | m2 m2 m2 m2 m2 m2 m2 m2 | Prepare batten floor for receiving a dry floor, remove any coatings present, rescrew loose battens, replace damaged ones. Depending on the requirements as drip protection, fit a layer _____________ (packing paper, glass fibre mat or the like) with 10 cm overlap. AQUAPANEL® Levelling Fill, installation thickness ________ mm (more than 60 mm), must be removed with a superelevation of 10% flat with the plane over gauges. Uneven areas, pipes or cables must be covered by at least 10 mm. Lay cover panels (e.g. soft timber fibres, mineral fibres, plasterboard in accordance with EN520; note material thickness for layer height), tight against one another, avoiding cross joints and shifted to the joints on the fill. Subsequently lay panels or chip panel strips in sections and mechanically compress the fill on top of this with a hand stamper or a surface vibrator. Lay AQUAPANEL® Cement Board Floor, 22 mm, cement-bonded dry floor element with surrounding slot, in accordance with the processing instructions of Knauf Aquapanel GmbH & Co. KG. Apply AQUAPANEL® Interior Primer in accordance with the processing instructions of Knauf Aquapanel GmbH & Co. KG. AQUAPANEL® Levelling Fill, maximum or minimum requirement per cm. |  |  |